## Slide 1: Guide to Virtual Private Networks - VPN’s
Simon Harper
Technical Consultant
Enterasys Networks - EMEA

## Slide 2: VPN’s Use IPSec to Protect Users against the following attacks:-
Spoofing – One machine or user on a network masquerades as another
Sniffing – An eavesdropper listens in on a transmission between users
Hijacking – Spoofing and other techniques are used to take control of a communications session, allowing the attacker to masquerade as one of the communicating parties

## Slide 3: Types of VPN Product
Router-based
Software-based
Firewall-based
Hardware optimised

## Slide 4: Types of VPN Uses
Remote Access
  PSTN, ISDN, ADSL, SDSL, Cable, Wireless
Site-to-site – Intranets
  Company branch offices, retail stores, WAN back-up
Site-to-site – Extranets
  Third party suppliers and partners

## Slide 5: Applications for VPN’s
More cost effective than traditional RAS – users make just a local call to an ISP Point Of Presence (POP)
Faster connection speed and more readily available links for site-to-site
Provides Triple DES encryption over Wireless
Can be used for WAN back-up
Provides a secure connection for Telecommuters who have access to ADSL - also provides a remote firewall functionality

## Slide 6: Tier 1 ISP - Global Internet Coverage

## Slide 7: Types of Central-Site VPN/ Firewall Topologies
VPN
Internet
Firewall
Internet
VPN
Firewall
Internet
VPN
Firewall
Internet
1
2
3

## Slide 8: Aurorean ™ Virtual Network Enterprise VPN
system updates, access policies, connection log
ANC
Aurorean Network Client
Management Channel
APS-3000/7000
Aurorean Policy Server
ANG-3000/7000
Aurorean Network
Gateway
Aurorean
Management
Software
M
RMS-5000
POP
LAN-Attached
Remote Facilities
Central Site
Remote Users
The Internet
Internet
Connection
POP
POP
POP
RTR
Analog
Modems
ISP
RAS
PSTN
Firewall
Authentication
Server
Direct Dial
Mobile Workers
RTS-5000
ISDN, xDSL, Cable Modems
Telecommuters
And SOHO
RTS-5000
IP and IPX
Notes: This diagram illustrates a typical EVPN remote access network with a central site facility on the left, remote user groups on the right, and the Internet cloud in the middle. Using an EVPN to augment or replace dedicated dial access to a RAS can cut tele-communications costs by 50% or more. EVPNs also enable the formation of large-scale communications networks by leveraging the global reach of the public Internet.
RiverWorks is an enterprise-class VPN that delivers a complete solution composed of central site hardware and remote user software. Dedicated hardware systems terminate thousands of EVPN tunnels and provide a sophisticated management platform for controlling the network These devices are called RiverWorks Tunnel Servers (RTS) and RiverWorks Management Servers (RMS). In addition, RiverPilot client software authenticates users and builds secure EVPN tunnels while performing the access management tasks defined by the central RiverWorks Management Server. A management channel established between the central site systems and remote user desktops delivers management information and system updates automatically.

## Slide 9: Remote Access
ANG 3000/7050
Aurorean Policy Server
Internet
Microsoft Certificate Authority
Native Windows Clients
Aurorean Client
Personal Firewall

## Slide 10: The Enterasys - Sygate Solution
Aurorean Client
Internet / WAN
ANG-110x
Small Office
Wireless LAN
Mobile User
RoamAbout NIC
Central Site
Learns Network Behavior
Applies Policy Management
Enforces Host-based Integrity
Prevents Network Access
ANG-7050
Personal Firewall
Sygate Secure Enterprise Suite
Personal Firewall
Personal Firewall
Access Point
Corporate Network

## Slide 11: Aurorean Software Client NAT/Proxy/Firewall Traversal

## Slide 12: Interoperability with Windows XP & 2000 – Single Sign-On
Tunnel Server
Aurorean 7050
Policy Server
APS 7000
Windows 2000
Active Directory
Windows 2000
IAS Server
Corporate Network
Internet
2 Factor
Authentication
Smart
Card

## Slide 13: Site-to-site
Internet
Internet
ANG-3000/7050
ANG-3000/7050
ANG-1102/1105
ANG-1102/1105
ANG-1102/1105
Peer-to-peer connection

## Slide 14: Interoperability
Cisco VPN 3005 Router
Nortel Contivity CES 600 Switch
CheckPoint 4.1 Firewall/ VPN-1
Internet
ANG-1102’s/1105’s
EZ-IPSec “one-click” configuration
Sell ANG-1102/1105 into existing VPN accounts

## Slide 15: Failure Points
Internet
X
1
1 Communications Interface
X
2
2 Access Line
X
3
3 Internet POP
X
4
4 Service Provider
X
5
5 Internet Connection
X
6
6 VPN Gateway
VPN Gateway
POP
POP
Virtual Private Network
Virtual Private Network
Notes: The conventional way of providing “high availability” is to offer hardware with dual power supplies and cooling fans. However, this approach does not provide an enterprise with true high availability, since a virtual private network is an end-to-end connection between remote users and the corporate network, and there are many potential points of failure throughout that connection path.
1. Communications Interface - The remote user may have forgotten to plug in his modem connection, or one of the communications interfaces in his machine may be inoperable.
2. Access Line - The remote user may utilize cable or DSL to access the Internet, but the provider may be experiencing a service outage. Increasingly, V.90 modems are being utilized as a backup to broadband access.
3. Internet POP - The ISP POP may be busy, or the POP phone number may have changed. There could even be a new area code for that exchange, or authentication failures at the POP may prevent access.
4. Service Provider - The ISP may be down, or could be providing very slow connections that impede productivity due to heavy congestion on the provider’s backbone.
5. Internet Connection - The corporate Internet pipe may be down because of a cut fiber connection.
6. VPN Gateway - Finally, the last potential point of failure in an end-to-end VPN connection is the VPN gateway itself. However, as you can see, there are many problem sources along the VPN connection path which could cause network downtime. All of these must be addressed when ensuring high availability for your virtual private network.

## Slide 16: Aurorean Virtual Network™ Enterprise VPN
Auto Link Recovery™ Architecture
RiverMaster 2
RTS-5000
210.15.15.3
RMS-5000
Aurorean VPN 2
PSTN
RAS
RADIUS
SecurID
AUTH
Aurorean VPN 1
Firewall
RiverMaster 1
M
Central Site
Remote Users
DIAL
Internet
210.15.15.2
RMS-5000
RTR
RTR
Applications
T1
DIAL
T1
CABLE
RTS-5000
Notes: This slide shows how the RiverWorks Enterprise VPN product suite is used to build an end-to-end virtual private network.
RiverPilot VPN client software is deployed on remote users’ desktops, and is used to connect to the local ISP and to create the secure, encrypted tunnel back to the corporation. At the central site, the RiverWorks Tunnel Server terminates and routes all remote user traffic, providing high-performance packet encryption and decryption. The RiverWorks Management Server contains all system level configurations and user and group policy settings, including processing authentication requests. Finally, the entire RiverWorks system is centrally controlled using the RiverMaster Management Application.
Auto Link Recovery adds a secondary RiverWorks system to the virtual private network. This includes a second RiverWorks Tunnel Server, RiverWorks Management Server, and RiverMaster Management Application. In this architecture, RiverPilot continues to tunnel into the primary RiverWorks system, but in the event that the system fails or is unreachable, RiverPilot automatically and transparently tunnels into the secondary RiverWorks system.
This achieves both hardware and service redundancy, ensuring the highest level of availability for your virtual private network end to end.

## Slide 17: Small Office / Home Office
AVN 1
AVN 2
Firewall
Aurorean
management
software
M
Central Site
Internet
RTR
RTR
Application Servers
T1
T1
SOHO
ANG1100
POP
workstations
DSL Modem
ISP 1
ISP 2
HUB
PPPoE
DHCP server
RTS-5000
RTS-5000
RTS-5000
RTS-5000

## Slide 18: Customer Example - University of Maryland University College
RTR
RAS
Firewall
RAS
Internet
ANG 7000
APS 7000
RTR
ANG 7000
APS 7000
Firewall
RTR
RAS
Primary Site to Site
Secondary Site to Site
RTR
ANG 7000
APS 7000
Firewall
RTR
ANG 7000
APS 7000
Firewall
ANG 7000
APS 7000
RTR
ANG 7000
APS 7000
Firewall
Firewall
Primary to Euro and Asia
Primary to USA and Asia
Primary to Euro and USA
Secondary to Euro and Asia
Secondary to Euro and USA
Secondary to USA and Asia
Japan
Germany
United States

## Slide 19: In-House or Managed Service VPN?
In-House Customer Premise Equipment (CPE) VPN
  ISP just provides Internet access
  Allows the use of multiple ISP’s
  Corporate IT staff manage user authentication
Managed Service VPN
  ISP manages VPN devices and client software
  Able to manage firewalls, user authentication and certificate authority

## Slide 20: IPSec VPN’s – Built for the Future
Additional Cryptographic Methods
  New cryptographic algorithms
Additional Protocols
  Being extended to encapsulate other protocols beyond IP
VPN integration with Public Key Infrastructure and a Certificate Authority

## Slide 21: VPN’s Conclusions - Benefits to Business
Allows business to exploit the low cost and ubiquity of the Internet
  Worldwide connectivity for its customers, partners and employees to corporate resources
VPN designs require minimum disruption to existing networks
  Implementation can be phased over a period of time to various sites and users
Benefits such as saving on call charges and increased business efficiency make VPN’s an attractive solution for many organisations

## Slide 22
Enterprise Class VPN - EVPN
Questions ?